## Slide 1
AS Solid materials
Divide the cards up equally among the group
Take it in turns to read out ONE property. The highest value wins the other cards.
Answer ALL questions at the bottom of each card

## Slide 2
Materials Top Trumps
Density | 7,135 kgm-3 | Malleability | 6
Hardness | 2.5 | Ductility | 5
Young modulus | 96 GPa | Flexibility | 2
Strength | 200x106 Pa | Toughness | 8
Materials Top Trumps
Density | 8,940 kgm-3 | Malleability | 7
Hardness | 3 | Ductility | 9
Young modulus | 120 GPa | Flexibility | 3
Strength | 220x106 Pa | Toughness | 6
Materials Top Trumps
Density | 1,950 kgm-3 | Malleability | 4
Hardness | 2 | Ductility | 0
Young modulus | 181x109 Nm-2 | Flexibility | 2
Strength | 4300 x106Pa | Toughness | 9
Materials Top Trumps
Density | 11,340 kgm-3 | Malleability | 9
Hardness | 1.5 | Ductility | 2
Young modulus | 16x109 Nm-2 | Flexibility | 4
Strength | 100 x106Pa | Toughness | 4
1. QUESTION: What is the definition of a brittle material?
2. QUESTION: How is the stiffness of a material calculated?
3. QUESTION: How is stored elastic energy calculated from a graph of Force applied (N) over extension of a material (m)?
4. QUESTION: What is hysteresis? How would this appear in a graph?
Zinc
Copper
Carbon Fibre
Lead

## Slide 3
Materials Top Trumps
Density | 8000 kgm-3 | Malleability | 6
Hardness | 4.5 | Ductility | 7
Young modulus | 110 GPa | Flexibility | 2
Strength | 2000 x106 Pa | Toughness | 8
Materials Top Trumps
Density | 1 kgm-3 | Malleability | 0
Hardness | 0 | Ductility | 0
Young modulus | 1 MPa | Flexibility | 0
Strength | 0.4x106 Pa | Toughness | 1
Materials Top Trumps
Density | 4,500kgm-3 | Malleability | 3
Hardness | 6 | Ductility | 7
Young modulus | 310x109 Nm-2 | Flexibility | 2
Strength | 10.4PGa | Toughness | 9
Materials Top Trumps
Density | 7,800 kgm-3 | Malleability | 6
Hardness | 4 | Ductility | 5
Young modulus | 210x109 Pa | Flexibility | 3
Strength | 3x106 Pa | Toughness | 7
5. QUESTION: Explain why the units of the Young Modulus can be either Nm-2 or Pa.
6. QUESTION: Why might a material be described as tough?
7. Task: Draw a stress strain graph for titanium.
8. Question: The compressive strength of marble is 112MPa. If a marble column holding up a roof of a temple is a cylinder supporting 1.43x107N, what is it’s minimum diameter?
Stainless Steel
Aerogel
Titanium
Iron

## Slide 4
Materials Top Trumps
Density | 1,100 kgm-3 | Malleability | 10
Hardness | 2 | Ductility | 0
Young modulus | 0.01x109 Nm-2 | Flexibility | 7
Strength | 15x106 Pa | Toughness | 7
Materials Top Trumps
Density | 2.7x103 kgm-3 | Malleability | 0
Hardness | 1.2 | Ductility | 0
Young modulus | 9.2Nm-2 | Flexibility | 2
Strength | 1x106 Pa | Toughness | 2
Materials Top Trumps
Density | 3.5x103 kgm-3 | Malleability | 0
Hardness | 10 | Ductility | 0
Young modulus | 1220x109 Nm-2 | Flexibility | 0
Strength | 1600x106 Pa | Toughness | 10
Materials Top Trumps
Density | 10 kgm-3 | Malleability | 2
Hardness | 10 | Ductility | 0
Young modulus | 1000 GPa | Flexibility | 1
Strength | 130 GPa | Toughness | 10
9. QUESTION: How is Young’s Modulus calculated?
10. TASK: Draw a stress-strain graph and plot two lines of different stiffness
11. QUESTION: Why is glass said to be brittle?
12. QUESTION: Name 3 malleable materials and state the definition of malleable.
Graphene
Diamond
Rubber
Graphite

## Slide 5
Materials Top Trumps
Density | 510 kgm-3 | Malleability | 2
Hardness | 2.5 | Ductility | 0
Young modulus | 9 GPa | Flexibility | 4
Strength | 40X106 Pa | Toughness | 5
Materials Top Trumps
Density | 2.8x103 kgm-3 | Malleability | 1
Hardness | 5.5 | Ductility | 0
Young modulus | 80x109 Nm-2 | Flexibility | 2
Strength | 33x106 Pa | Toughness | 8
Materials Top Trumps
Density | 8520 kgm-3 | Malleability | 6
Hardness | 3 | Ductility | 3
Young modulus | 100x109 Nm-2 | Flexibility | 2
Strength | 550x106 Pa | Toughness | 8.5
Materials Top Trumps
Density | 2000 kgm-3 | Malleability | 3
Hardness | 3 | Ductility | 0
Young modulus | 14 x109 Nm-2 | Flexibility | 4
Strength | 130x106 Pa | Toughness | 8
13. QUESTION: What are the units of tensile strain?
14. Task: Draw a stress-strain graph for glass
15. QUESTION: What is necking and when does it occur in material tests?
16. QUESTION: How is compressive stress calculated and what are the units?
Pine wood
Glass
Brass
Bone

## Slide 6
Materials Top Trumps
Density | 1050 kgm-3 | Malleability | 8
Hardness | 1 | Ductility | 0
Young modulus | 7,500 Nm-2 | Flexibility | 8
Strength | 20 MPa | Toughness | 1
Skin
Materials Top Trumps
Density | 1120 kgm-3 | Malleability | 9
Hardness | 1 | Ductility | 1
Young modulus | 2 GNm-2 | Flexibility | 8
Strength | 580 x106 Pa | Toughness | 9
Materials Top Trumps
Density | 75kgm-3 | Malleability | 2
Hardness | 0 | Ductility | 0
Young modulus | 3.5x109 Nm-2 | Flexibility | 5
Strength | 50 MPa | Toughness | 1
Materials Top Trumps
Density | 3970 kgm-3 | Malleability | 0
Hardness | 7 | Ductility | 0
Young modulus | 435x109 Nm-2 | Flexibility | 0
Strength | 1.9 GPa | Toughness | 9
Sapphire
17. QUESTION: Define shear stress and give an example of it.
18. QUESTION: Is a material that is brittle also weak?
19. QUESTION: What can be said to be the opposite of brittleness?
20. QUESTION: ________ materials show resistance to plastic deformation
Polystyrene
Nylon

## Slide 7
Materials Top Trumps
Density | 2,400 kgm-3 | Malleability | 0
Hardness | 5 | Ductility | 0
Young modulus | 85 GPa | Flexibility | 1
Strength | 3 MPa | Toughness | 7
Materials Top Trumps
Density | 2,700 kgm-3 | Malleability | 6
Hardness | 3 | Ductility | 3
Young modulus | 69 GNm-2 | Flexibility | 7
Strength | 50x106 Pa | Toughness | 7
Materials Top Trumps
Density | 1,300 kgm-3 | Malleability | 8
Hardness | 0 | Ductility | 0
Young modulus | 300 MPa | Flexibility | 10
Strength | 1 GPa | Toughness | 9
Materials Top Trumps
Density | 0.07 kgm-3 | Malleability | 7
Hardness | 0 | Ductility | 0
Young modulus | Nm-2 | Flexibility | 9
Strength | 380x106 Pa | Toughness | 8
21. QUESTION: What’s the definition of compressive strength?
22. QUESTION: What’s the definition of compressive strain?
23. QUESTION: Are all malleable materials tough? Explain.
24. QUESTION: Give the material properties necessary for a) Aeroplane wings b) Electrical wiring and c) Building construction
Spider silk
Human Hair
Concrete
Aluminium

## Slide 8: QUESTIONS
QUESTION: What is the definition of a brittle material?
QUESTION: How is the stiffness of a material calculated?
QUESTION: How is stored elastic energy calculated from a graph of Force applied (N) over extension of a material (m)?
QUESTION: What is hysteresis? How would this appear in a graph?
QUESTION: Explain why the units of the Young Modulus can be either Nm-2 or Pa.
QUESTION: Why might a material be described as tough?
Task: Draw a stress strain graph for titanium.
Question: The compressive strength of marble is 112MPa. If a marble column holding up a roof of a temple is a cylinder supporting 1.43x107N, what is it’s minimum diameter?
QUESTION: How is Young’s Modulus calculated?
TASK: Draw a stress-strain graph and plot two lines of different stiffness
QUESTION: Why is glass said to be brittle?
QUESTION: Name 3 malleable materials and state the definition of malleable.
QUESTION: What are the units of tensile strain?
Task: Draw a stress-strain graph for glass
QUESTION: What is necking and when does it occur in material tests?
QUESTION: How is compressive stress calculated and what are the units?
QUESTION: Define shear stress and give an example of it.
QUESTION: Is a material that is brittle also weak?
QUESTION: What can be said to be the opposite of brittleness?
QUESTION: ________ materials show resistance to plastic deformation
QUESTION: What’s the definition of compressive strength?
QUESTION: What’s the definition of compressive strain?
QUESTION: Are all malleable materials tough? Explain.
QUESTION: Give the material properties necessary for a) Aeroplane wings b) Electrical wiring and c) Building construction
Notes: http://en.wikipedia.org/wiki/List_of_materials_properties#Mechanical_properties
Hardness is Mohs Hardness
All other values are subjective estimates - made up

## Slide 9: ANSWERS
QUESTION: A lot of stress for little strain. Shatters upon larger applied forces?
QUESTION: F = kx, where k is the stiffness
QUESTION: Area under graph = Nm = Joules
QUESTION: What is hysteresis? How would this appear in a graph?
QUESTION: Explain why the units of the Young Modulus can be either Nm-2 or Pa.
QUESTION: Why might a material be described as tough?
Task: Draw a stress strain graph for titanium.
Question: The compressive strength of marble is 112MPa. If a marble column holding up a roof of a temple is a cylinder supporting 1.43x107N, what is it’s minimum diameter? – 0.4m
QUESTION: How is Young’s Modulus calculated?
TASK: Draw a stress-strain graph and plot two lines of different stiffness
QUESTION: Why is glass said to be brittle?
QUESTION: Name 3 malleable materials and state the definition of malleable.
QUESTION: What are the units of tensile strain?
Task: Draw a stress-strain graph for glass
QUESTION: What is necking and when does it occur in material tests?
QUESTION: How is compressive stress calculated and what are the units?
QUESTION: Define shear stress and give an example of it.
QUESTION: Is a material that is brittle also weak?
QUESTION: What can be said to be the opposite of brittleness?
QUESTION: ________ materials show resistance to plastic deformation
QUESTION: What’s the definition of compressive strength?
QUESTION: What’s the definition of compressive strain?
QUESTION: Are all malleable materials tough? Explain.
QUESTION: Give the material properties necessary for a) Aeroplane wings b) Electrical wiring and c) Building construction
Notes: http://en.wikipedia.org/wiki/List_of_materials_properties#Mechanical_properties
Hardness is Mohs Hardness
All other values are subjective estimates - made up